## Slide 1: Emergency exit recognizer
Course: Multimedia Systems
Student: Savev David

## Slide 2: Introduction
Goals:
Recognition of emergency exit shields within image frames (.png or .jpg);
Acoustically signal the direction to follow to leave the building.

## Slide 3: Analysis
Emergency exit shield = closed area predominantly with green pixels;
Green area = rectangular shape (convex polygon with 4 vertices);
Within the rectangle, the arrow color ≠ background color;
Arrow = concave polygon with 7 or 9 vertices.

## Slide 4: OpenCV
Library used for computer vision, image and video processing operations.
Pros:
  Well documented;
  supported among several programming languages (Python, C++, Java);
  widely adopted (community support, forums).

## Slide 5: Image processing I
Recognition of emergency exit shield

## Slide 6: Image processing II
Arrow direction recognition

## Slide 7: Contour approximation
Due to the blurring or image rotation, a wrong contour polygon may be extracted (hence  wrong number of vertices).
ApproxPolyDP(contour, ε) method permits the approximation of the contour, where ε parameters indicates the accuracy of the algorithm (distance from contour to its approximation).

## Slide 8: Arrow tip
Which one is the tip of the arrow among 7 or 9 vertices? The tip is the point which has the biggest distance to the closest neighbour.
arr_dist = []
foreach vertex1 in vertices do:
min_dist = ∞
foreach vertex2 in vertices do:
dist_x = abs(vertex1.x - vertex2.x)
dist_y = abs(vertex1.y – vertex2.y)
res = dist_x + dist_y
if res not 0 and res < min_dist do:
min_dist = res
arr_dist.append(min_dist)
indx = index(max(arr_dist))
return vertices[indx]

## Slide 9: Arrow direction
In order to compute the direction of the arrow, we need the x, y coordinates of the tip and the center of the arrow.
dist_x = abs(tip_x - center_x)
dist_y = abs(tip_y - center_y)
if dist_x > dist_y do:
if arrow_x - center_x < 0 do:
#Arrow pointing left
else do:
#Arrow pointing right
else do:
if arrow_y - center_y < 0 do:
#Arrow pointing up
else:
#Arrow pointing down

## Slide 10: GUI
Developed with help of the tkinter library.
Main features:
Upload of .jpg or .png images;
Not processed image plotted on the left;
Processed image and all its features (contour, vertices, center) plotted on the right;
Possibility to plot intermediate steps of the processing.
In every case, an mp3 file indicating the direction to follow is played.

## Slide 11: Images

## Slide 12: Problems
Reconnaissance value ≅ 70-75% of the images that were collected as samples
20-25% of the cases, false positives and false negatives.
Error ε, due to:
Different conditions (image colors, image rotation, blurring);
Different tuning parameters (green color range, dimension of filtering matrixes, threshold, approximation of polygon vertices, upper bound of the shape matching between contours).

## Slide 13: Conclusion
In order to increase the “Reconnaissance” percentage, further investigation, analysis, refinement and tuning is needed.
Since NO Machine Learning was used, a future implementation may take also these techniques into account and may be adapted to work also on video streams.